## Slide 2: GPU Architecture: Threads, Warps, Blocks, and Grid
Thread: The simplest unit of computation in CUDA. Threads are what actually perform the instructions in the code.
Warp: A collection of 32 threads. All threads in a warp execute in lockstep. Not directly accessible in code, but it is fundamental to understand in order to maximize performance.
Block: A collection of an arbitrary number of threads. The exact number can be specified in code. Blocks can have up to three dimensions, which provide the threadIdx.x, threadIdx.y, threadIdx.z, blockDim.x, blockDim.y, and blockDim.z variables. The block in this image is a 8 x 4 block (one warp) of threads. A block can have 1024 threads at most.
Grid: A collection of an arbitrary number of blocks. The exact number can be specified in code. Grids can have up to three dimensions, which provide the blockIdx.x, blockIdx.y, blockIdx.z, gridDim.x, gridDim.y, and gridDim.z variables. The grid in this image is a 2 x 2 grid of blocks.

## Slide 3: GPU Architecture: Streaming Multiprocessor Memory Resources
Streaming Multiprocessor (SM): Except for global memory, all GPU resources are local to a SM. The number of SMs per GPU depends on hardware generation. SMs can run at most 48 warps (1536 threads), or at most 8 blocks. Blocks cannot be divided between SMs.
Register Memory: Local to a specific thread. Fastest memory available, but also the least plentiful. The total amount of registers on an SM is shared equally across all threads running on the SM so the registers needed per thread contributes to the maximum number of threads that can run at once.
Shared emory: Local to a specific block. Slower than register memory, but more of it is available. The total amount of shared memory available is shared equally across all blocks running on the SM so the amount of shared memory needed per block contributes to the maximum number of threads that can run at once. Analogous to RAM in normal computing.

## Slide 4: GPU Architecture: Global Memory
Global Memory: Available to all threads on a GPU. The slowest memory type available, but also the most plentiful. Analogous to hard drive space in normal computing. Data must be stored “nicely” so that the performance hit from using it it minimized.