## Slide 1: Computational Chemistry in Parallel
Dylan Hennessey

## Slide 2: Dirac Equation
First accurate merging of quantum mechanics and special relativity was done by Dirac in 1928
Gave an equation for a free electron
Negative energy electrons (positrons)
Positive energy electrons (electrons)
P. A. M. Dirac. The quantum theory of the electron. Proc. R. Soc. Lond. A, 117(778):610–624, 1928.

## Slide 3: Relativistic Two-Electron Integrals
Spinor symmetry
Basis functions
Function returning 2
integers
Large component
Small component
O. Matsuoka and Y. Watanabe. An atomic Dirac-Fock-Roothaan program. Comput. Phys. Commun, 139(2):218 – 234, 2001

## Slide 4: GPU Architecture: Threads, Warps, Blocks, and Grid
Thread: The simplest unit of computation in CUDA. Threads are what actually perform the instructions in the code.
Warp: A collection of 32 threads. All threads in a warp execute in lockstep. Not directly accessible in code, but it is fundamental to understand in order to maximize performance.
Block: A collection of an arbitrary number of threads. The exact number can be specified in code. Blocks can have up to three dimensions, which provide the threadIdx.x, threadIdx.y, threadIdx.z, blockDim.x, blockDim.y, and blockDim.z variables. The block in this image is a 8 x 4 block (one warp) of threads. A block can have 1024 threads at most.
Grid: A collection of an arbitrary number of blocks. The exact number can be specified in code. Grids can have up to three dimensions, which provide the blockIdx.x, blockIdx.y, blockIdx.z, gridDim.x, gridDim.y, and gridDim.z variables. The grid in this image is a 2 x 2 grid of blocks.

## Slide 5: GPU Architecture: Streaming Multiprocessor Memory Resources
Streaming Multiprocessor (SM): Except for global memory, all GPU resources are local to a SM. The number of SMs per GPU depends on hardware generation. SMs can run at most 48 warps (1536 threads), or at most 8 blocks. Blocks cannot be divided between SMs.
Register Memory: Local to a specific thread. Fastest memory available, but also the least plentiful. The total amount of registers on an SM is shared equally across all threads running on the SM so the registers needed per thread contributes to the maximum number of threads that can run at once.
Shared Memory: Local to a specific block. Slower than register memory, but more of it is available. The total amount of shared memory available is shared equally across all blocks running on the SM so the amount of shared memory needed per block contributes to the maximum number of threads that can run at once. Analogous to RAM in normal computing.

## Slide 6: GPU Architecture: Global Memory
Global Memory: Available to all threads on a GPU. The slowest memory type available, but also the most plentiful. Analogous to hard drive space in normal computing. Data should be stored contiguously in order to minimize the performance hit from using it.

## Slide 7: Matrix Multiplication Example
A
B
C
X
=
The matrices A, B, and C are stored in row-major order. So the rows of A and C can be read/written effectively. The columns of B cannot be read effectively.

## Slide 8: Matrix Multiplication Example
Global Memory
Shared Memory
Register Memory
Using a block size of 32x32 and a grid size of 2x2
Step 2: Copy the first tiles of matrix A and B into the shared memory
Step 3: Each thread independently multiplies the needed elements of A and B and stores the result in the register memory
Step 1: Map threads to elements of matrix C
Step 4: Copy next set of tiles into the shared memory and repeat step 3
Step 4: Copy result from the shared memory to the global memory

## Slide 9: cudaDFRATOM
cudaDFRATOM is a program in written in CUDA Fortran and Fortran 90
Allows for the optimization of Well-Tempered Basis Sets on GPUs
Based of Matsuoka’s DFRATOM program
SCF was carried out using the cuBLAS and cuSOLVER libraries
Custom code was written to calculate the two-electron integrals on GPUs
O. Matsuoka and Y. Watanabe. An atomic Dirac-Fock-Roothaan program. Comput. Phys. Commun, 139(2):218 – 234, 2001

## Slide 10: Two-Electron Algorithm
Six indices to loop over and a non-trivial method of
determining their maximum values makes this algorithm difficult to parallelize

## Slide 11: Three-Dimensional Solution
Map λ to threadIdx.x, p to threadIdx.y and q to threadIdx.z
Block dimensions would be (1, 32, 32)
Grid dimensions would be

## Slide 12: Three-Dimensional Solution
Basis set of size (30,25,25,20,20,15,15).
The blockDim = (1,32,32) and gridDim = (7,1,1)
Workload is not distributed to threads very well.

## Slide 13: Two-Dimensional Solution
Better because each thread is now only calculating
one set of integrals
Still have issues with blocks containing idle threads

## Slide 14: One-Dimensional Solution
Best solution because all threads have the same work load and only the last block has the possibility of having idle threads

## Slide 15: Mapping Threads
Basis set of size (3, 2)
Basis set of size (3, 2)

## Slide 16: Mapping Threads: Find X and Y
Basis set of size (3, 2)
Use binary search to find the indices from just i
First try to find x. It’s easy to determine that the minimum value of x is 1 and the maximum value is 9. We guess that the value of x is 5.
Minimum and maximum values of i are 11 and 15 so x must be larger. Guess that x is 7.
Minimum and maximum values of i are 22 and 28 so we know that the thread must be in this column

## Slide 17: Mapping Threads: Find λ, p, q, μ, r, and s
Basis set of size (3, 2)
Know that minimum and maximum values of λ are 1 and 2
so guess that λ is 1
Determine minimum and maximum values of x are 1 and
6 < x = 7, so λ must be 2
Know that minimum and maximum values of p are 1 and 2
so guess that p is 1
Determine only possible value of x is 7 meaning p = 1
Get q from
Perform the exact same operations using y to get μ, r, and s

## Slide 18: Advantages of Using this Method
Can handle arbitrary basis set sizes
Faster than pre-calculating order on CPU then uploading to GPU
If the number of integrals to calculate is small, then it only needs to be performed once
If the number of integrals to calculate is large, then it can quickly be recalculated as needed
Can be written to an read from the global memory effectively

## Slide 19: Resource Usage

## Slide 20: 2eint performance

## Slide 21: Conclusion and Future Work
The cudaDFRATOM program uses effective method of mapping threads to two-electron integrals, allowing
as much of the GPU hardware to be used as possible
Mapping algorithm has a negligible effect on total time to compute the two-electron integrals and
scales well with the number of integrals
Total speedup limits to ~20x faster than CPU calculations
Algorithm could be modified to use constant memory
Algorithm could be modified to allow for mapping of other point groups
Algorithm could be modified to allow for direct SCF